## Slide 1: Global Carbon Budget
Published on 13 November 2024
2022
PowerPoint version 1.0
The GCP is a Global Research Project of
and a Research Partner of
2024

## Slide 2: Acknowledgements
The work presented here has been possible thanks to the enormous observational and modelling efforts of the institutions and networks below
Atmospheric CO2 datasets
NOAA/GML (Lan et al., 2024)
Scripps (Keeling et al., 1976)
Atmospheric O2 datasets
Scripps (Keeling 2024)
Fossil CO2 emissions
Andrew and Peters, 2024
CDIAC-FF (Hefner and Marland, 2024)
UNFCCC 2024
Energy Institute 2024
Consumption emissions
Peters et al., 2011
GTAP (Narayanan et al., 2015)
Land-use change
Houghton and Castanho 2023
BLUE (Hansis et al., 2015)
OSCAR (Gasser et al., 2020)
LUCE (Qin et al., 2024)
GFED4 (van der Werf et al., 2017)
FAO-FRA and FAOSTAT
HYDE (Klein Goldewijk et al., 2017)
LUH2 (Hurtt et al., 2020)
MapBiomas (Souza et al., 2020)
Land models
CABLE-POP | CLASSIC | CLM6.0 | DLEM | eDV3 | ELM | IBIS | ISAM | ISBA-CTRIP | JSBACH | JULES-ES | LPJ-GUESS | LPJml | LPJ-wsl | LPX-Bern | OCN | ORCHIDEEv3 | SDGVM | VISIT | CARDAMOM
Climate forcing CRU (Harris et al., 2014) | JRA-55 (Kobayashi et al., 2015)
Ocean models
NEMO-PlankTOM12 | NEMO4.2-PISCES (IPSL) | MICOM-HAMOCC (NorESM1-OCv1.2) | MPIOM-HAMOCC6 | NEMO3.6-PISCESv2-gas (CNRM) | FESOM2.1-REcoM3 | MOM6-COBALT (Princeton) | CESM-ETHZ | MRI-ESM2-3 | ACCESS (CSIRO)
fCO2 based ocean flux products
VLIZ-SOMFFN | Jena-MLS | CMEMS-LSCE-FFNNv2 | UExP-FNN-U | NIES-ML3 | JMA-MLR | OceanSODA-ETHZv2 | LDEO-HPD CSIR-ML6
Surface Ocean CO2 Atlas SOCATv2024
Atmospheric inversions
Jena CarboScope | CAMS | CarbonTracker Europe (CTE) | NISMON-CO₂ | CT-NOAA | CMS-Flux | CAMS-Satellite | GONGGA | COLA | GCASv2 | UoE in-situ | IAPCAS | MIROC4-ACTM | NTFVAR
Earth system models
CanESM5 | EC-Earth3-CC | IPSL-CM6A-CO2-LR | MIROC-ES2L | MPI-ESM1-2-LRCan
Full references provided in Friedlingstein et al 2024

## Slide 3: Contributors 119 people | 86 organisations | 19 countries
P Friedlingstein | M O'Sullivan | MW Jones | RM Andrew | J Hauck | P Landschützer C Le Quéré | H Li | IT Luijkx | A Olsen | GP Peters | W Peters | J Pongratz | C Schwingshackl S Sitch | JG Canadell | P Ciais | RB Jackson SR Alin | A Arneth | V Arora | NR Bates | M Becker | N Bellouin | CF Berghoff | HC Bittig L Bopp | P Cadule | K Campbell | M Chamberlain | N Chandra | F Chevallier | LP Chini TH Colligan | J Decayeux | L Djeutchouang | X Dou | C Duran Rojas | K Enyo | W Evans A Fay | RA Feely | DJ Ford | A Foster | T Gasser | M Gehlen | J Ghattas | T Gkritzalis G Grassi | L Gregor | N Gruber | Ö Gürses | I Harris | M Hefner | J Heinke | GC Hurtt | Y Iida T Ilyina | AR Jacobson | AK Jain | T Jarníková | A Jersild | F Jiang | Z Jin | E Kato | RF Keeling K Klein Goldewijk | J Knauer | J Korsbakken | SK Lauvset | N Lefèvre | Z Liu | J Liu | L Ma S Maksyutov | G Marland | N Mayot | P McGuire | N Metzl | NM Monacci | EJ Morgan S Nakaoka | C Neill | Y Niwa | T Nutzel | L Olivier | T Ono | PI Palmer | D Pierrot | Z Qin L Resplandy | A Roobaert | C Rödenbeck | J Schwinger | TL Smallman | S Smith R Sospedra-Alfonso | T Steinhoff | Q Sun | AJ Sutton | R Séférian | S Takao | H Tatebe H Tian | B Tilbrook | E Tourigny | H Tsujino | F Tubiello | G van der Werf | R Wanninkhof W Xuhui | D Yang | X Yang | Z Yu | W Yuan | X Yue | S Zaehle | N Zeng | J Zeng
Atlas Team Members at LSCE, France
P Ciais | P Brockmann
Communications Team
A Hayward | G Davies | A Morrison C Bartman | N Hawtin | K Mansell

## Slide 4: Data Access and Additional Resources
More information, data sources and data files:
https://globalcarbonbudget.org/carbonbudget
More information, data sources and data files:
www.globalcarbonatlas.org
(co-funded in part by BNP Paribas Foundation)

## Slide 5: Download of figures and data
Figures and data for most slides available from tinyurl.com/GCB24figs and from https://globalcarbonbudget.org/carbonbudget
Global Carbon Budget
Additional country figures

## Slide 6
All the data is shown in billion tonnes CO2 (GtCO2)
1 Gigatonne (Gt) = 1 billion tonnes = 1×1015g = 1 Petagram (Pg)
1 kg carbon (C) = 3.664 kg carbon dioxide (CO2)
1 GtC = 3.664 billion tonnes CO2 = 3.664 GtCO2
(Figures are available from https://globalcarbonbudget.org/carbonbudget)
Most figures in this presentation are available for download as PNG, PDF and SVG files from tinyurl.com/GCB24figs along with the data required to produce them.
Disclaimer
The Global Carbon Budget and the information presented here are intended for those interested in learning about the carbon cycle, and how human activities are changing it. The information contained herein is provided as a public service, with the understanding that the Global Carbon Project team make no warranties, either expressed or implied, concerning the accuracy, completeness, reliability, or suitability of the information.

## Slide 7: License
Our intention is that these figures and data are used. That’s why they’re released under the Creative Commons Attribution 4.0 International license. Simply put, you may freely copy and modify these figures and data, and use them in both commercial and non-commercial works, as long as you give credit to the Global Carbon Project.
If you’re just tweeting a figure or using a figure in a presentation, then it already says at the bottom that it’s by the Global Carbon Project, so you’re good to go! If you use the data directly or modify the figure, then you will need to make sure the attribution is in place.
For details on the license, visit the Creative Commons website.
Suggested citation for use in a book: “Used with permission of the Global Carbon Project under the Creative Commons Attribution 4.0 International license.”

## Slide 8: Atmospheric CO2 concentration
The global CO2 concentration increased from ~277 ppm in 1750 to 422.5 ppm in 2024 (up 52%)
Globally averaged surface atmospheric CO2 concentration. Data from: NOAA-GML after 1980;
the Scripps Institution of Oceanography before 1980 Source: NOAA-GML; Scripps Institution of Oceanography; Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 9: Anthropogenic perturbation of the global carbon cycle
Perturbation of the global carbon cycle caused by anthropogenic activities, global annual average for the decade 2014–2023 (GtCO2/yr)
CDR here refers to Carbon Dioxide Removal besides those associated with land-use that are accounted for in the Land-use change estimate. The budget imbalance is the difference between the estimated emissions and sinks. Source: NOAA-GML; Friedlingstein et al 2024; Canadell et al 2021 (IPCC AR6 WG1 Chapter 5); Global Carbon Project 2024

## Slide 10: Key Highlights in 2024

## Slide 11: Global Fossil CO2 Emissions
Global fossil CO2 emissions: 37.0 ± 2 GtCO2 in 2023, 66% over 1990 Projection for 2024: 37.4 ± 2 GtCO2, 0.8% [-0.2% to +1.7%] higher than 2023
The 2024 projection is based on preliminary data and modelling. The global total includes a cement carbonation sink of 0.8 GtCO2. Source: Friedlingstein et al 2024; Global Carbon Project 2024
Uncertainty is ±5% for one standard deviation (IPCC “likely” range)

## Slide 12: Emissions Projections for 2024
There are sharp contrasts between the projected emissions changes for the top emitters
The 2024 projections are based on preliminary data and modelling. ‘Bunkers’ are fossil fuels used for international shipping and aviation Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 13: Fossil CO2 emissions growth: 2022–2024
Emissions are expected to increase in India, international aviation and the combined rest of the world (Others) in 2024, decline in USA and the EU, and increase marginally in China
The 2024 projections are based on preliminary data and modelling. Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 14: Summary of fossil CO2 emissions in 2023 and 2024
Region / Country | 2023 emissions (billion tonnes/yr) | 2023 growth (percent) | 2024 projected emissions growth (percent) | 2024 projected emissions (billion tonnes/yr)
China | 11.9 | +4.9% | +0.1% | 11.9
USA | 4.9 | -3.3% | -0.9% | 4.9
India | 3.1 | +8.2% | +3.7% | 3.2
EU27 | 2.5 | -8.4% | -2.8% | 2.4
International bunkers* | 1.1 | +9.4% | +7.8% | 1.2
All others | 14.3 | +0.1% | +1.2 | 14.5
World | 37.8 | +1.3% | +0.7% | 38.2
World (incl. cement carbonation) | 37.0 | +1.4% | +0.8% | 37.4
*Emissions from use of international aviation and maritime shipping bunker fuels are not usually included in national totals. Cement carbonation sink only included in global (World) estimate. Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 15: Land-use change emissions
Land-use change emissions are 4.1 ± 2.6 GtCO2 per year for 2014–2023, and show a negative trend in the last two decades, but estimates are still highly uncertain. Projection for 2024: 4.2 ± 2.6 GtCO2
Estimates from four bookkeeping models Source: Friedlingstein et al 2024; Global Carbon Project 2024
Indonesian fires

## Slide 16: Land-use change emissions
Combined land-use change emissions from Brazil, Indonesia, and the Democratic Republic of the Congo make up 60% of the global net land-use change emissions
Estimates from four bookkeeping models Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 17: Forecast of global atmospheric CO2 concentration
The global atmospheric CO2 concentration is forecast to average 422.5 parts per million (ppm) in 2024, increasing by 2.9 ppm.
Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 18: Mauna Loa atmospheric CO2
Atmospheric CO2 concentration has increased every single year, including in 2020 – despite the drop in fossil CO2 emissions – because of continued emissions
Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 19: Shared Socioeconomic Pathways (SSPs)
The SSPs were designed to span the range of potential outcomes. Total CO2 emissions are currently tracking in the middle of the range. The temperature outcomes are based on assessed scenarios in IPCC AR6 Working Group I.
This set of quantified SSPs are based on the output of six Integrated Assessment Models (AIM/CGE, GCAM, IMAGE, MESSAGE, REMIND, WITCH). Net emissions include those from land-use change and bioenergy with CCS. Source: Riahi et al. 2016; Rogelj et al. 2018; IIASA SSP Database; IAMC; Global Carbon Project 2024

## Slide 20: Global fossil CO2 emissions

## Slide 21: Global fossil CO2 emissions
Global fossil CO2 emissions have risen steadily over the last decades. Emissions are set to grow again in 2024.
The 2024 projection is based on preliminary data and modelling. Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 22: Global fossil CO2 emissions
For the last 100 years, it has generally taken a crisis to drive global emissions reductions. To stabilise temperatures, intentional, planned, sustained global reductions must begin.
The 2024 projection is based on preliminary data and modelling. Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 23: Fossil CO2 emission intensity
Global CO2 emissions growth has generally resumed quickly from global crises. Emission intensity has steadily declined but not sufficiently to offset economic growth.
Each trend line is based on the five years before the crisis and extended to five years after. Economic activity is measured in purchasing power parity (PPP) terms in 2017 US dollars.
Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 24: Fossil CO2 emissions by country

## Slide 25: Top emitters: Fossil CO2 emissions to 2023
The top six emitters in 2023 covered 68% of global emissions China 32%, United States 13%, India 8%, EU 7%, Russia 5%, and Japan 3%
International aviation and maritime shipping (bunker fuels) contributed 3.0% of global emissions in 2023.
Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 26: Top emitters: Fossil CO2 emissions per capita to 2023
Countries have a broad range of per capita emissions reflecting their national circumstances
International aviation and maritime shipping (bunker fuels) contributed 3.0% of global emissions in 2023.
Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 27: Fossil CO2 emissions — Kaya decomposition
Globally, decarbonisation and declines in energy per GDP are largely responsible for the reduced growth rate in emissions over the last decade. 2020 was a clear outlier with a sharp decline in GDP.
Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 28: Historical cumulative fossil CO2 emissions
The USA and EU have the highest accumulated fossil CO2 emissions since 1850, but China is a close third.
Calculated using territorial emissions.
Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 29: Fossil CO2 emissions by source

## Slide 30: Fossil CO2 emissions by source
Share of global fossil CO2 emissions in 2024: coal (41%), oil (32%), gas (21%), cement (4%), flaring and others (2%, not shown)
The 2024 projection is based on preliminary data and modelling. Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 31: Fossil CO2 emissions growth: 2022–2024
Global emissions from oil continued to rebound in both 2023 and 2024 with recovery of aviation. In 2023 natural gas grew slowly because of supply constraints but returns to growth in 2024. Coal continues to climb.
Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 32: Fossil CO2 emissions by source
Emissions by category from 2000 to 2024, with growth rates indicated for the more recent period of 2019 to 2024 Coal use has returned to growth, and both coal and oil declined sharply in the pandemic year 2020
Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 33: Energy use by source
Consumption of natural gas was flat in 2023, but oil exceeded its pre-pandemic level. Renewable energy continued to grow, but needs to grow even faster to replace fossil energy consumption.
This figure shows “primary energy” using the substitution method (non-fossil sources are scaled up by an assumed fossil efficiency of approximately 0.38) Source: Energy Institute 2024; Global Carbon Project 2024

## Slide 34: Fossil CO2 emission by source for top emitters

## Slide 35: Fossil CO2 emissions in China
China’s coal and oil consumption levelled off in 2024, while emissions from gas continue to grow strongly
Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 36: Fossil CO2 emissions in USA
The USA’s emissions from coal continued their long decline in 2024, to their lowest level since 1902, as the transition to natural gas and growth in renewables continue. Emissions from oil are still below 2019’s level.
Source: EIA 2023; Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 37: Fossil CO2 emissions in India
India’s emissions continue to grow strongly in 2024. Increases in solar and wind capacity were far from sufficient to meet a large increase in power demand as the economy grows strongly.
Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 38: Fossil CO2 emissions in the European Union
The EU’s emissions from coal continue to fall strongly in 2024, a result of strong growth in renewables but also economic headwinds caused by high energy costs.
Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 39: Fossil CO2 emissions in Rest of World
In the rest of the world, emissions from coal and oil grow slightly while natural gas jumps again. Oil in international aviation grew strongly again, nearing pre-pandemic levels.
The Rest of the World is the global total less China, US, EU, and India. Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 40: Cement carbonation sink

## Slide 41: Cement carbonation sink
The production of cement results in ‘process’ emissions of CO2 from the chemical decomposition of carbonates. During its lifetime, cement re-absorbs some CO2 from the atmosphere.
Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 42: Land-use change emissions

## Slide 43: Land-use change emissions
Land-use change emissions were 4.1 ± 2.6 GtCO2 per year for 2014–2023, and show a negative trend in the last two decades, but estimates are still highly uncertain.
Estimates from four bookkeeping models Source: Friedlingstein et al 2024; Global Carbon Project 2024
Indonesian fires
Net land-use emissions are the result of multiple anthropogenic activities on land that lead to CO₂ emissions or removals
Projection for 2024:
4.2 ± 2.6 GtCO2

## Slide 44: Land-use change emissions
Annual emissions from permanent deforestation declined over 2014–2023 but remain high at around 3.7 GtCO2.
Carbon dioxide removals through permanent af/reforestation are 1.9 GtCO2 per year over the same period.
Estimates from four bookkeeping models Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 45: Regional patterns of land-use change emissions
Land-use emissions are high in the tropics, driven largely by deforestation. Net sinks occur in regions of re/afforestation such as parts of Europe and China.
Estimates from four bookkeeping models Source: Friedlingstein et al 2024; Global Carbon Project 2024
The peak in Indonesia in 1997 was the Indonesian peat fires.
The top three emitters over 2014–2023 – Brazil, Indonesia, and the Democratic Republic of the Congo – contribute 60% of the global net land-use emissions.
Land-use emissions, decadal average 2014–2023

## Slide 46: Linking global models to country reports
Mapping of global carbon cycle model land flux definitions to the definition of the LULUCF net flux used in national Greenhouse Gas Inventories (NGHGI) reported to UNFCCC
Source: Friedlingstein et al 2024; Global Carbon Project 2024
Figure from Grassi et al., ESSD 2023
When natural fluxes on managed forests (-6.7 GtCO2 per year for 2014–2023) are added to land-use emissions (4.1 GtCO2 per year), the GCB2024 estimates (-2.6 GtCO2 per year) are very similar to the country-reported data (-2.8 GtCO2 per year), linking the anthropogenic carbon budget estimates of land CO2 fluxes directly to the Global Stocktake as part of UNFCCC Paris Agreement.

## Slide 47: Total global emissions
Total global emissions, projected to reach 41.6 ± 3.2 GtCO2 in 2024, 51% over 1990 Percentage land-use change: 42% in 1960, 10% averaged 2014–2023
Land-use change estimates from four bookkeeping models, using fire-based variability from 1997 Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 48: Carbon Dioxide Removal
Vegetation-based CDR estimates from GCB2024
CDR not based on vegetation from the State of CDR report (2024)
Equivalent to ~1 millionth of annual Fossil CO2 emissions
Equivalent to ~5% of annual Fossil CO2 emissions
1.9 GtCO2 per year
0.004 MtCO2 per year
0.03 MtCO2 per year

## Slide 49: Closing the Global Carbon Budget

## Slide 50: Fate of anthropogenic CO2 emissions (2014–2023)
29%
11.7 GtCO2/yr
Source: Friedlingstein et al 2024; Global Carbon Project 2024
26%
10.5 GtCO2/yr
35.6 GtCO2/yr
90%
10%
4.1 GtCO2/yr
19.2 GtCO2/yr
48%
Sources = Sinks
4%
-1.6 GtCO2/yr
Budget Imbalance: (the difference between estimated sources & sinks)

## Slide 51: Global carbon budget
Carbon emissions are partitioned among the atmosphere and carbon sinks on land and in the ocean The “imbalance” between total emissions and total sinks is an active area of research
Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 52: Changes in the budget over time
The sinks have continued to grow with increasing emissions, but climate change will affect carbon cycle processes in a way that will exacerbate the increase of CO2 in the atmosphere
The budget imbalance is the total emissions minus the estimated growth in the atmosphere, land and ocean.
It reflects the limits of our understanding of the carbon cycle.
Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 53: Global carbon budget
Fossil emissions dominate in the Northern Hemisphere, while land-use emissions are important in the tropics. The North Atlantic and Southern Ocean are carbon sinks while the tropical ocean is a source of CO2. Tropical, temperate and boreal forest are the main terrestrial carbon sinks
Source: Friedlingstein et al 2024; Global Carbon Project 2024
CO2 Source
CO2 Sink
CO2 Source
CO2 Sink
CO2 Source
CO2 Sink

## Slide 54: Atmospheric concentration
The atmospheric concentration growth rate has increased steadily. The high growth in 1987, 1998, & 2015–16 reflect a strong El Niño, which weakens the land sink.
Source: NOAA-GML; Friedlingstein et al 2024; Global Carbon Project 2024
Projected 2024

## Slide 55: Airborne Fraction
The airborne fraction is the proportion of the total annual CO2 emissions that remains in the atmosphere.
The rest of the CO2 emissions are removed by the land and ocean sinks. Around 45% of CO2 emissions remain in the atmosphere despite sustained growth in CO2 emissions.
Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 56: Ocean sink
The ocean carbon sink, estimated by Global Ocean Biogeochemical Models and observation-based data products,
amounts to 10.5 ± 1.5 GtCO2/yr for 2014–2023 and 10.6 ± 1.5 GtCO2/yr in 2023.
The ocean sink increased in 2023, in line with the expected sink response to the 2023 El Niño conditions.
This is after no growth since 2019 due to a triple La Niña event during 2020–2022.
Source: SOCATv2023; Bakker et al 2016; Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 57: Terrestrial sink
Source: Friedlingstein et al 2024; Global Carbon Project 2024
The land carbon sink, estimated by Dynamic Global Vegetation Models, was 11.7 ± 3.2 GtCO2/yr
during 2014–2023. The effects of El Niño that developed in late 2023 and early 2024 reduced the land CO2 sink to 8.4 GtCO2 in 2023, 28% below its decadal mean.
The total CO2 fluxes on land (including land-use change) are also constrained by atmospheric inversions.

## Slide 58: Land and ocean sinks — Effects of CO2 vs climate change
Process models suggest that increasing atmospheric CO2 drives the land and ocean sinks while climate change reduces the carbon sinks; the climate effect is largest in tropical and semi-arid land ecosystems.
Globally during 2014–2023, climate change reduced the land sink by ~27% and the ocean sink by 6%.
Source: Friedlingstein et al 2024; Global Carbon Project 2024
CO2 Source
CO2 Sink

## Slide 59: Land and ocean sinks — Estimates from atmospheric inversions
Both atmospheric CO2 inversions and atmospheric oxygen allow to estimate the land and ocean carbon fluxes, independently from the land and ocean process-based models, confirming the global carbon budget estimates of the land and ocean partitioning of anthropogenic CO2
Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 60: Total land and ocean fluxes
Source: Friedlingstein et al 2024; Global Carbon Project 2024
Bottom-up estimates and top-down atmospheric inversions broadly agree on the land and ocean sinks at large regional scales.
The interannual variability in the global total CO₂ flux is largely due to the variability of the land sink in the tropics.

## Slide 61: Remaining carbon budget imbalance
The budget imbalance is the carbon left after adding independent estimates for total emissions, minus the atmospheric growth rate and estimates for the land and ocean carbon sinks using models constrained by observations
Source: Friedlingstein et al 2024; Global Carbon Project 2024
Large and unexplained variability in the global carbon balance caused by uncertainty and understanding hinder independent verification of reported CO2 emissions
positive values mean overestimated emissions and/or underestimated sinks

## Slide 62: Global carbon budget
The cumulative contributions to the global carbon budget from 1850 The carbon imbalance represents the gap in our current understanding of sources & sinks
Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 63: Remaining carbon budget
The remaining carbon budget to limit global warming to 1.5°C , 1.7°C and 2°C is
235 GtCO2, 585 GtCO2, and 1110 GtCO2 respectively, equivalent to 6, 14 and 27 years from 2025. 2650 GtCO2 have been emitted since 1850
The remaining carbon budgets are the average of two estimates (IPCC AR6 and Forster et al., 2023), both updated by removing the most recent emissions. Quantities are subject to additional uncertainties e.g., future mitigation choices of non-CO2 emissions
Source: IPCC AR6 WG1; Forster et al., 2023; Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 64: Remaining carbon budget
Global CO2 emissions must reach zero to limit global warming
Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 65: Acknowledgements

## Slide 66: Acknowledgements
The work presented in the Global Carbon Budget 2024 has been possible thanks to the contributions of hundreds of people involved in observational networks, modelling, and synthesis efforts.
We thank the institutions and agencies that provide support for individuals and funding that enable the collaborative effort of bringing all components together in the carbon budget effort.
We thank the sponsors of the GCP and GCP support and liaison offices.
We also want to thank the many funding agencies that supported this coordinated effort and the individual components of this release. A full list is provided in Friedlingstein et al. 2024.
https://essd.copernicus.org/preprints/essd-2024-519
We also thanks the Fondation BNP Paribas for supporting the Global Carbon Atlas and the Integrated Carbon Observation System (ICOS) for hosting our data.
This presentation was created by Robbie Andrew and Pierre Friedlingstein with Pep Canadell, Glen Peters and Corinne Le Quéré in support of the international carbon research community.

## Slide 67: Additional Figures

## Slide 68: Additional Figures Fossil CO2

## Slide 69: Emissions changes 2022–2024
Emissions from coal in China and India have been a core reason for global growth. Both 2023 and 2024 were marked by post-pandemic recovery in international aviation (bunkers).
Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 70: Top emitters: Fossil CO2 Emissions
Emissions by country from 2000 to 2024, with the growth rates indicated for the more recent period of 2019 to 2024
Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 71: Per capita CO2 emissions
Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 72: Top emitters: Fossil CO2 Emission Intensity
Emission intensity (emission per unit economic output) generally declines over time. In many countries, these declines are insufficient to overcome economic growth.
GDP is measured in purchasing power parity (PPP) terms in 2017 US dollars.
Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 73: Kaya decomposition
The Kaya decomposition illustrates that relative decoupling of economic growth from CO2 emissions is driven by improved energy intensity (Energy/GDP) and, recently, carbon intensity of energy (CO2/Energy)
GDP: Gross Domestic Product (economic activity) Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 74: Fossil CO2 emission intensity
The 10 largest economies have a wide range of emission intensity of economic activity
Emission intensity: Fossil CO2 emissions divided by Gross Domestic Product (GDP) Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 75: Fossil CO2 Emissions per capita
The 10 most populous countries span a wide range of development and emissions per capita
Emission per capita: Fossil CO2 emissions divided by population Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 76: Alternative rankings of countries
The responsibility of individual countries depends on perspective. Bars indicate fossil CO2 emissions, population, and GDP.
GDP: Gross Domestic Product in Market Exchange Rates (MER) and Purchasing Power Parity (PPP) Source: United Nations; Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 77: Breakdown of global fossil CO2 emissions by country
Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 78: Fossil CO2 emissions by continent
Asia dominates global fossil CO2 emissions, while emissions in North America are of similar size to those in Europe, and the Middle East is growing rapidly.
Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 79: Fossil CO2 emissions by continent: per capita
Oceania and North America have the highest per capita emissions, while the Middle East has recently overtaken Europe. Africa has by far the lowest emissions per capita.
Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 80: Additional Figures Consumption-based Emissions
Consumption–based emissions allocate emissions to the location that goods and services are consumed
Consumption-based emissions = Production/Territorial-based emissions minus emissions embodied in exports plus the emissions embodied in imports

## Slide 81: Consumption-based emissions (carbon footprint)
Allocating fossil CO2 emissions to consumption provides an alternative perspective. USA and EU are net importers of embodied emissions, China and India are net exporters.
Consumption-based emissions are calculated by adjusting the
standard emissions estimates to account for international trade Source: Peters et al 2011; Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 82: Consumption-based emissions per person
The differences between fossil CO2 emissions per capita is larger than the differences between consumption and territorial emissions.
Consumption-based emissions are calculated by adjusting the
standard emissions estimates to account for international trade Source: Peters et al 2011; Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 83: Consumption-based emissions (carbon footprint)
Transfers of emissions embodied in trade between OECD and non-OECD countries grew slowly during the 2000’s, declined to 2015 and have been relatively flat since then.
Source: Peters et al 2011; Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 84: Major flows from production to consumption (2017) — Land Use Change CO2
Global distribution of land-use change emissions embodied in trade: Arrows show largest flows from location of generation of emissions to location of consumption of agricultural and forestry goods.
Values for 2017. EU27 is treated as one region. Units: MtCO2 Source: Hong et al 2022
MtCO2 yr-1

## Slide 85: Additional Figures Historical Emissions

## Slide 86: Total global emissions by source
Land-use change was the dominant source of annual CO2 emissions until around 1950. Fossil CO2 emissions now dominate global changes.
Others: Emissions from cement production, gas flaring and carbonate decomposition Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 87: Historical cumulative emissions by source
Others: Emissions from cement production, gas flaring and carbonate decomposition Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 88: Historical cumulative fossil CO2 emissions by country
‘All others’ includes all other countries along with emissions from international aviation and maritime shipping Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 89: Historical cumulative emissions by continent
Cumulative fossil CO2 emissions (1850–2023). North America and Europe have contributed the most cumulative emissions, but Asia is growing fast
The figure excludes emissions from international aviation and maritime shipping Source: Friedlingstein et al 2024; Global Carbon Project 2024

## Slide 90: Additional Figures Energy Use

## Slide 91: Energy use by source
Energy consumption by fuel source from 2000 to 2023, with growth rates indicated for the more recent period of 2018 to 2023
This figure shows “primary energy” using the BP substitution method (non-fossil sources are scaled up by an assumed fossil efficiency of approximately 0.38) Source: Energy Institute, 2023; Global Carbon Project 2024

## Slide 92: Energy use by source: China
Coal consumption in energy units has returned to peak levels, while consumption of all other energy sources is growing strongly
This figure shows “primary energy” using the BP substitution method (non-fossil sources are scaled up by an assumed fossil efficiency of approximately 0.38) Source: Energy Institute, 2023; Global Carbon Project 2024

## Slide 93: Energy use by source: USA
Coal consumption has declined sharply in recent years with the shale gas boom
and strong renewables growth. Output from nuclear power is slowly declining as stations are retired.
This figure shows “primary energy” using the BP substitution method (non-fossil sources are scaled up by an assumed fossil efficiency of approximately 0.38) Source: Energy Institute, 2023; Global Carbon Project 2024

## Slide 94: Energy use by source: India
Pandemic year 2020 temporarily interrupted India’s strong growth in energy consumption. Consumption of coal and oil dominate.
This figure shows “primary energy” using the BP substitution method (non-fossil sources are scaled up by an assumed fossil efficiency of approximately 0.38) Source: Energy Institute, 2023; Global Carbon Project 2024

## Slide 95: Energy use by source: EU
Consumption of both oil and gas has rebounded in recent years, while coal continues to decline.
Renewables are growing strongly, now providing more energy than nuclear power.
This figure shows “primary energy” using the BP substitution method (non-fossil sources are scaled up by an assumed fossil efficiency of approximately 0.38) Source: Energy Institute, 2023; Global Carbon Project 2024